NEW METHODS AND INSTRUMENTS IN

QUALITY RISK MANAGEMENT

Gábor DIMÉNY

“Gedeon Richter Romania” S.A. Tg. Mures

gdimeny@gedeon-richter.ro

Abstract: The Quality Risk Management is a valuable component of the efficient Quality Management Systems. This approach has a specific importance in a quality risk sensitive industries. The paper presents a review of new statistical methods and instruments for Quality Risk Management, theoretical elements and practical case study. Based on the fundamental importance of the process stability and capability, are defined quality risk functions through Partitioned Multi-objective Quality Risk Method, mathematical formulation of the risk of quality non-conformities, the quality risk represented by the application of different economical optimization models in product manufacturing.

Keywords: quality management, quality risk management

1.  INTRODUCTION

In a quality risk-sensitive industries (e.g. nuclear energy, aviation, car manufacturing, drug manufacturing, etc.) the manufactured product (or process) nonconformities can represent a serious risk to the client. Therefore, these products are manufactured in a strongly regulated environment, through the entire life-cycle of the product, respectively through the whole general product realization process. The present status and the new trends show, that the inherent quality risk management existing in Quality Management Systems in theses areas is not satisfactory and a systematic, regulated process is needed. In the same time, in addition to the qualitative risk management methods, efficient quantitative, statistics based methods and instruments are required (Dimény,2007).

2.  STATISTICAL TOOLS FOR QUALITY RISK ANALYSIS

2.1. Partitioned Multi-objective Risk Method

As a new mathematical instrument for quality risk analysis, the Partitioned Multi-objective Risk Method (PMRM) (Haimes, 2004) can be one of these statistical tools. The need for the method is originating in the fallacy of the expected value when it is used as the sole criterion for risk in decision making. A conditional expectation is defined as the expected value of a random variable, given that this value lies within some pre-specified probability range. The concept of the expected value of damage, in the PMRM, is extended to generate multiple conditional expected value functions, each associated with a particular range of exceedance probabilities or their corresponding range of damage severities.

The quality parameter distribution, in general can be considered normal. Thus, the probability density function  for variable x, respectively the standard probability density function  [and standard distribution function ] for the transformed variable u, for three partitioned zones are represented in Fig.2. The mathematical relations for,  and  are represented by the relations (1)…(3) (Dimény,2007).

;      ;         (1),(2),(3)

where  is the process mean, σ the standard deviation. It can be observed, that zone I. and II. represent in fact conformance with specifications, that is, the quality parameter is situated inside the tolerance area. However, for certain cases, establishing uniformity requirements can be useful to emphasize the exceedance of alert limits (,), respectively (, ). Zone III. with high severity and low probability, is in fact the area of quality nonconformities (rejects).

For these zones, it can be established the quality risk functions, , i= 1,2,3, characterizing the severity of the risks. The resulting functions, in conjunction with the traditional expected value, provide a family of risk measures associated with a particular risk management policy. The quality parameter conditional expected value approach through PMRM, may be an important tool for studying “extreme” events with low exceedance probability but high severity, because in high-quality manufacturing a defect can be considered an extreme event, respectively with an extremely rare appearance.

2.2. Quality Risk Functions

The quality risk function  for zone III. has two one-sided formulations:  for exceedance of the upper tolerance limit, and  for the lower limit. These relations and their related probabilities, for normal distribution are expressed by relations (4)…(7), where , .(Haimes, 2004, Dimény,2007)

; Prob (4),(5)

(6)

Prob                                                              (7)

The above presented quality functions represent the conditional expected value of the quality parameter. Using these functions, respectively the quality risk definition, that is, the combination (product) of the probability of occurrence of the nonconformity and the severity of that nonconformity, the related relations for the quality risk (appearance of non-conform products/rejects by exceeding the specified limits U and L) can be expressed by the relations (8) and (9):

;                       (8),(9)

The unconditional expected value is expressed by the well known relation . The function  is reserved for the quality management cost. These five risk functions can be used in a multi-objective optimization process, for supporting a quality decision analysis (Haimes, 2004, Dimény,2007).

The probability of non-conform product appearance (defects, rejects) in a technological process can be characterized through process capability (or process capability indices Cp), that is, the process’ ability to produce products with pre-specified parameters, between specified tolerance limits.

The process mean (expected value) shift is a process instability causing factor, affecting the process capability and thus influencing the quality risk (the appearance of non-conform products, with quality parameters situating out-side of  specified/tolerance limits – see Fig. 2.). Defining the quality risk functions and the related probabilities for two cases of exceedance the tolerance limits (L, respectively U), the mathematical relations of quality risk for non-conforming quality parameter appearing are presented by the relations (10),(11).

;          (10),(11)

In the same time can be demonstrated the following relation, respectively an increasing of quality risk in case of process mean shift:

+  > 2                                 (12)

2.3. Case study of production process

Process optimization mathematical model (filling process), based on minimizing of production expected cost with reprocessing, is expressed by the relation (13), where  is the expected production cost per product produced (Dimény,2007, Golhar and Pollock,1988):

(13)

The values for optimal expected cost,  şi  are obtained by solving the system of equations (14),(15), R, C, M are process parameters.

In the following example an ointment tube filling process will be presented. Two cases will be comparatively studied, for establishing the process mean, respectively the tolerance limits (Fig. 5.): a.) is the generally used „symmetrical case” (process mean on the center of tolerance area) and b.) the „optimum case” (, ).

(14)

(15)

The process mean for symmetrical case is 45 g, the specified lower limit is 43,65 g. Relations for production cost calculus are presented by (16) and (17).

(16)

(17)

The following process parameters are known: filled material cost C= 0,1 lei/g; product reprocessing cost R=0,2 RON/unit.

Process parameter M is calculated by the relation M=R/Cσ, and for solving the equation system (14)-(15), a computer program is utilized. [Dimény,2007]

Quality risks are calculated by relations (8),(9) and the case study is realized for different process capabilities Cp. The graphical representations for production costs and quality risks, related to the appearance of non-conform products/rejects by exceeding the specified limits U and L, are presented in Fig. 4. and 5.

2.4 Conclusions

It can be observed that the „price paying” for the economical optimum is an increase in quality risk, respectively in increasing of global exceedance probability of tolerance limits, expressed by the relation (18), and the production management has to consider this important aspect. Additionally, use of QRM can improve the decision making, if a quality problem arises.

>                                (18)

Effective QRM can facilitate better and more informed decisions (Dimény,2007), can provide regulators with greater assurance of a company’s ability to deal with potential risks.

3.  REFERENCES

Dimény, G. (2007) Cercetări şi contribuţii privind aplicarea tehnicilor şi metodelor moderne ale ingineriei şi managementului calităţii în producţia de medicamente (Researches and contributions to application of modern quality management and engineering methods and techniques in the pharmaceutical manufacturing), Teză de doctorat (PhD thesis), Cluj- Napoca : Technical University

Haimes, Y. (2004)  Risk Modeling, Assessment and Management, New Jersey : John Wiley & Sons Inc.

Golhar, D., Pollock, S. (1988) Determination of the Optimal Process Mean and the Upper Limit  for a Canning Problem, Journal of Quality Technology, 20 (3): 188-19

# Text boxes

u

0

III.

II.

I.

II.

III.

Fig. 1. Partitioned zones representation

Fig. 3.  Symmetrical and optimum cases

a. symmetrical case

b. optimum  case

Fig. 4. Production costs as functions of Cp

Fig. 5. Quality risks as functions of Cp

μ+

Fig. 2. Process mean shift representation

u

0